## Slide 1: Independent Components Analysis with the JADE algorithm
Douglas N. Rutledge
Muséum National d'Histoire Naturelle, Paris
Laboratoire de Chimie Analytique-Faculté de Pharmacie Paris Sud, Université Paris-Saclay
douglas.neil.rutledge@gmail.com

## Slide 2: Multivariate Data Analysis
Variables
Samples
(objects) (individuals)
Line Vectors
Column Vectors

## Slide 3: A matrix as points in space
X = -1.00 0.00 0.50
1.00 -1.00 -1.00
-0.50 1.00 -1.00
1.00 1.00 -1.00
2.00 -0.50 1.00
-1
0
1
2
-1
-0.5
0
0.5
1
-1
-0.5
0.0
0.5
1

## Slide 4
Principal Components Analysis
Pearson, 1901

## Slide 5
Principal Components Analysis
Samples projected onto space defined by variables
- if NO information → spherical distribution
→ NO preferred axes

## Slide 6
Principal Components Analysis
Samples projected onto space defined by variables
- if information → non-spherical distribution
→ preferred axes
PCA

## Slide 7: “Blind Source Separation”
Variables
Observed Sensor Signals
Row Vectors

## Slide 8
Principal Components Analysis (PCA)
data matrix points in the multivariate space
Independent Components Analysis (ICA)
data matrix a set of observed signals, where
    each observed sensor signal is the weighted sum of pure source signals
    the weighting coefficients are proportions of the source signals
Independent Components Analysis
x1 = a11*s1 + a12*s2 x2 = a21*s1 + a22*s2
…
In matrix notation : X = A*S

## Slide 9: Example
Two Independent Sources
Two mixtures
aij ... Proportion of source signal sj in observed signal xi

## Slide 10
The objective of ICA is to find "physically significant" vectors.
Hypotheses :
1) No reason for the variations in one pure signal to depend in any way on the variations in another pure signal
Pure signal sources should therefore be « independent »
2) The measured signals being combinations of several independants sources, they should be more gaussian than the sources (Central Limit Theorem)

## Slide 11
“Nongaussian is independent”: Central Limit Theorem The measured signals being combinations of several independants sources, they should be more gaussian than the sources Idea of ICA is to search for sources the least gaussian possible
Need to find a criterion to define the « gaussianity » of a signals : Kurtosis Negentropy Mutual information Complexity …

## Slide 12: ICA Principal (Non-Gaussian is Independent)
Key to estimating A is non-gaussianity
The distribution of a sum of independent random variables tends toward a Gaussian distribution (by CLT)
f(s1) f(s2) f(x1) = f(s1 +s2)
Where w is one of the rows of matrix W :
y is a linear combination of si, with weights given by zi.
Since sum of two independent r.v. is more gaussian than individual r.v., so zTs is more gaussian than either si
zTs becomes least gaussian when equal to one of si
So we take w as a vector which maximizes the non-gaussianity of wTx
.

## Slide 13: Measures of Non-Gaussianity
Quantitative measure of non-gaussianity for ICA estimation
Kurtosis : gauss=0 (sensitive to outliers)
Entropy : gauss=largest
Neg-entropy : gauss = 0 (difficult to estimate)
Approximations
where v is a standard gaussian random variable and :

## Slide 14
ICA : - decomposition of a set of vectors into linear components that are “as independent as possible”
“Independence” : - goes beyond (second-order) decorrelation involves the non-Gaussianity of the data

## Slide 15
“Independent” versus “non-correlated”
Deux variables x et y sont indépendantes si,
quelles que soient les valeurs non nulles a et b,
r(x^a, y^b) = 0
Dans le cas présenté,
si a=2 et b=1, r=1
donc x et y ne sont pas indépendantes.

## Slide 16
ICA attempts to recover the original signals by estimating a linear transformation, using a criterion that measures statistical independence among the sources This may be achieved by the use of higher-order information that can be extracted from the densities of the data PCA does not really look for (and usually does not find) components with physical reality Why not ? - PCA finds “direction of greatest dispersion of the samples” - this is the wrong direction for “signal separation” !

## Slide 17
A simulated example

## Slide 18
Initial data matrix
Matrix rows
Histograms

## Slide 19
PCA applied to the example
Loadings
Histograms

## Slide 20
Source Signals
Histograms
ICA applied to the example

## Slide 21
ICA calculates a demixing matrix, W W approximates A-1 , the inverse mixing matrix The pure component signals are recovered from the measured mixed signals by : S = W*X The trick is to calculate W when we only have X !
Procedure

## Slide 22
Many algorithms available : FastICA : numerical gradient search Projection Pursuit : interestingly structured vectors Complexity Pursuit : minimise common information JADE : based on “cumulants” ….
Calculating the demixing matrix

## Slide 23
JADE was developed by Cardoso et al. in 1993 [1].
A blind source separation method to extract independent non-Gaussian sources from signal mixtures with Gaussian noise
Based on the construction of a fourth-order cumulant array from the data
It is freely downloadable from http://www2.iap.fr/users/cardoso/compsep_classic.html
JADE
(Joint Approximate Diagonalization of Eigenmatrices)
[1] Cardoso and Souloumiac, IEE proceedings-F 140 (6) (1993), 362-370

## Slide 24
For a set of values : x 2° order auto-cumulant : s2(x) = Cum2{x, x} = E{x2} 4° order auto-cumulant kx(x) = Cum4{x, x, x, x} = E{x4} − 3.E2{x2}
Cumulants

## Slide 25
Cumulants can be expressed in tensor form. A tensor can be seen as a generalization of the notion of matrices. Cumulant tensors are a generalization of covariance matrices.
The main diagonal of cumulants tensors are auto-cumulants and non-diagonal elements are cross-cumulants. Statistically mutually independent vectors (components) give : - null cross-cumulants - maximum auto-cumulants
Cumulants

## Slide 26
In PCA :
The Eigenvalue decomposition of a covariance matrix results in its diagonalization, i.e. the cancellation of its non-diagonal terms.
In JADE :
A generalization of this methodology was proposed by Cardoso and Souloumiac to diagonalise fourth-order cumulants tensors.
Cumulants

## Slide 27
In the simple case of 3 observed signal vectors : x1, x2, x3 and 2 pure source signals : s1, s2 where : x1 = a11. s1 + a12. s2 x2 = a21. s1 + a22. s2 x3 = a31. s1 + a32. s2 k(x1) = Cum4{x1, x1, x1, x1} = E{x14} − 3.E2{x12} k(x1) = a114 . [E{s14} − 3.E2{s12}] + a124 . [E{s24} − 3.E2{s22}] k(x1) = a114 . k(s1) + a124 . k(s2)
Cumulants

## Slide 28
For the 3 observed signal vectors : x1, x2, x3 Create a four-way array with dimensions [3, 3, 3, 3] Each of the 81 elements is the mean of products of the vectors. For vi, vj, vk, vl = x1, x2, x3 Cum4{vi, vj, vk, vl} = E{vivjvkvl} − E{vivj} . E{vkvl} − E{vivk} . E{vjvl} − E{vivl} . E{vjvk}
4th-order Cumulants

## Slide 29
For vi, vj, vk, vl = xp (p=1:3) Cum4{p, p, p, p} = E{xp4} − E{xp2} . E{xp2} − E{xp2} . E{xp2} − E{xp2} . E{xp2} Cum4{p, p, p, p} = mean (xp4) − mean (xp2) . mean (xp2) − mean (xp2) . mean (xp2) − mean (xp2) . mean (xp2) Cum4{p, p, p, p} = mean (xp4) − 3
3 Auto-Cumulants 3 different values

## Slide 30
For vi, vj = xp et vk, vl = xq (p=1:3, q=1:3, p≠q ) Cum4{p, p, q, q} = E{xp2xq2} − E{xp2} . E{xq2} − E{xpxq} . E{xpxq} − E{xpxq} . E{xpxq} Cum4{p, p, q, q} = mean (xp2xq2) − mean (xp2) . mean (xp2) − mean (xpxq) . mean (xpxq) − mean (xpxq) . mean (xpxq) Cum4{p, p, q, q} = mean (xp2xq2) − 1
18 Even Cross-Cumulants 3 different values

## Slide 31
For vi= xp et vj, vk, vl = xq (p=1:3, q=1:3, p≠q) Cum4{p, q, q, q} = E{xpxq3} − E{xpxq} . E{xq2} − E{xpxq} . E{xq2} − E{xpxq} . E{xq2} Cum4{p, q, q, q} = mean (xpxq3) − mean (xpxq) . mean (xp2) − mean (xpxq) . mean (xq2) − mean (xpxq) . mean (xq2) Cum4{p, q, q, q} = mean (xpxq3) − 0
60 Odd Cross-Cumulants 9 different values

## Slide 32
Initial X matrix
Scores of first PCs of X
Scaled Scores of X
Smaller, whitened X matrix

## Slide 33
4-way tensor of cumulants

## Slide 34
Initial orthogonal matrices to project cumulants

## Slide 35
Eigenmatrices of cumulants

## Slide 36
Joint diagonalization using the Jacobi algorithm, based on Givens rotation matrices : Minimize the sum of squares of the “off-diagonal" 4th-order cumulants (i.e. the cumulants between different signals)
JADE

## Slide 37
Diagonalised matrices

## Slide 38
The JADE algorithm:
  a multi-step procedure






## Slide 39
Summary of JADE
PCA
Scale
(x l-1/2)
X
T
U
Diagonalise
(Rotate)
M
M*
V
Calculate
Cumulants
Decompose
Tensor
M
U
x
X

## Slide 40
JADE
U
Rotate
Scores
V
W
x
x
S
W
X
Calculate
Signals
S'
X
Calculate
Prop’ns
S'
S
-1
A

## Slide 41: Connection between PCA and ICA
Jade performs a rotation of the PCA Loadings vecctors
so as to maximze their non-gaussianity
(and therefore their independence)

## Slide 42: PCA & ICA on 100 Mid-Infrared spectra
Samples : a single polystyrene film
Mid-IR spectra taken at end of production line
Acquired from 4000cm-1 to 400cm-1, at 1 cm-1
Pre-treatment of spectra : - normalised between 0 and 1 - neither centred nor standardised

## Slide 43
Information Hidden in MIR Spectra
Source : R.Aries, D. Lidiard, R. Spragg, Spectrosc. Internat., 2(3) 41-44

## Slide 44
Mean spectrum

## Slide 45
CO2 & H2O

## Slide 46
CO2 & H2O

## Slide 48
Interferogram & derivative

## Slide 49
Interferogram & derivative

## Slide 50
ICA in JADE is a rotation of PCA Loadings to maximize their non-gaussianity
So we can do a PCA and then introduce the Loadings into JADE
Can be very useful when the X matrix is very tall ! (replace thousands of spectra by a small number of Loadings)
The link between PCA and ICA

## Slide 57
The Signals extracted by JADE applied to the PCA Loadings are exactly the same as those extracted by JADE applied to X (because the first step in JADE is a PCA on X)
So we can recover the ICA Proportions using the same equation as in JADE
Calculating the ICA Proportions
S'
X
Calculate
Prop’ns
S'
S
-1
A

## Slide 58
Extracted vectors have a physico-chemical meaning
ICA can be used to eliminate artefacts
ICA can be applied to all kinds of signals, including multi-way signals:
- Unfold the signals
- Calculate the ICA model on the matrix of one-dimensional signals
- Fold the ICs back
Advantages of ICA

## Slide 59
Different results may be obtained using different algorithms
Different results may be produced as a function of the number of Independent Components (ICs) extracted
Therefore importance of determining the number of ICs !
Difficulties with ICA

## Slide 60
PCA does not look for (and usually does not find) components with direct physical meaning
ICA tries to recover the original signals by estimating a linear transformation, using a criterion that measures statistical independence among the sources
This is done using higher-order information that can be extracted from the densities of the data
ICA can be applied to all types of data, including multi-way data
- D.N. Rutledge, D. Jouan-Rimbaud Bouveresse, Independent Components Analysis with the JADE algorithm Trends in Analytical Chemistry, 50, (2013) 22–32
- D. Jouan-Rimbaud Bouveresse, D.N.Rutledge
"Independent Components Analysis: Theory And Applications“ in Resolving Spectral Mixtures, (ed. C. Ruckebusch)
Elsevier Science Publishers, Amsterdam, 2017, pp. 225-278
Conclusion